## Slide 2
Fixed mislabeled GND pin on Raspberry Pi Header (Pin 38)

## Slide 3: GPS I2C & SPI Lines
Thicker Traces, Lower Resistance
Greater Spacing
Ground Plane Shielding
Added Vias To Reduce Ground Impedance, Improved Shielding

## Slide 4: Old Accelerometer Layouts
Decoupling Capacitors
  Far from the chips
  Located along common power line, reducing effectiveness
Unused pins are left floating
SPI lines and I2C lines
  Cross over each other
  Unnecessarily small and long
LEDs are powered directly off data lines, reducing signal integrity and power

## Slide 5: New Accelerometer Layout
Decoupling Capacitors
  Closer to power pins
  Individual 3V3 connections
Unused Pins Connected To Pulldown Resistors, Optional Pins Have Test Points
SPI and I2C lines
  Do Not Cross, Not Even Nearby
  Thicker Traces
  Isolated With Ground Plane In Between
  Added Vias To Add Shielding Inside Substrate
LEDs moved off data lines, connected directly to Raspberry Pi

## Slide 6: New Accelerometer Layouts