## Slide 1: MRDT Nav Board
Thomas Francois
Katherine Dunlap
Nithin Vijay

## Slide 2: Old Schematic
Use of Global Labels
  Dangerous Practice
Doesn’t Show Signal Flow
Incorrect Input For Raspberry Pi
  Mislabeled GND (Pin 38)
No Page Information
Cluttered Accelerometer Symbols, Unnecessary NC Pins
LEDs Powered Directly Off Data Lines, Reducing Signal Integrity And Power
No Pull-Down Resistors On I2C Lines

## Slide 3: New Schematic
Moved IMUs And Voltage Regulators To Hierarchical Sheets
  Improved Simplicity Of System Overview Page
  Reduced Clutter, Improved Scalability
Used Official KiCAD Raspberry Pi Header Symbol, Improved Molex Symbol
Use Of Bus Lines for I2C, UART, and SPI
  Improves Understanding Of System Data Flow
LEDs moved off data lines, connected directly to Raspberry Pi
Added Pull-Down Resistors To I2C
Added Page Information

## Slide 4: Accelerometer Component Sheets
Added Pull-Down Resistors To Unused Pins
Removed Do Not Connect Pins, Declutters Symbols
Added Test Points To GPIO and Interrupt Pins
  For Future Debug, Easier Modification For Future Features

## Slide 5: Voltage Regulator Component Sheets
Moved To Component Sheets For Simplicity Of Main Overview Page

## Slide 6: GPS I2C & UART Lines
Thicker Traces, Lower Resistance
Greater Spacing
Ground Plane Shielding Between Traces
Added Vias To Reduce Ground Impedance, Improved Shielding Inside Substrate
For Added Shielding:
  UART Routed On Top Layer
  I2C Routed On Bottom Layer
OLD
NEW

## Slide 7: Old Accelerometer Layout
Decoupling Capacitors
  Far from the chips
  Located along common power line, reducing effectiveness
Unused Pins Are Left Floating
  Including Interrupt Pin
SPI, I2C, And UART Lines
  Cross over each other
  Unnecessarily small and long
LEDs are powered directly off data lines, reducing signal integrity and power

## Slide 8: New Accelerometer Layout
Decoupling Capacitors
  Closer to power pins
  Individual 3V3 connections
Unused Pins Connected To Pulldown Resistors, Optional Pins Have Test Points
SPI and I2C lines
  Do Not Cross, Not Even Nearby
  Thicker Traces
  Isolated With Ground Plane In Between Signals
  Vias Added To Isolate From UART Lines
  Added Vias To Add Shielding Inside Substrate
LEDs moved off data lines, connected directly to Raspberry Pi
Added Test Points To GPIO and Interrupt Pins

## Slide 9: Improved LEDs
Moved off data lines, connected directly to Raspberry Pi
Will be controlled in software, just like Ethernet status LEDs
Labeled
Old Layout
New Layout

## Slide 10: PCB Renderings

## Slide 12: Bill Of Materials
39 Components
  45 Listed, But Test Points, Solder Jumpers, and Raspberry Pi Pins Don’t Count
Same components from previous board, all can be salvaged for $0
BOM is same from previous board, consult previous documentation to order new components
Item | Qty | Reference(s) | Value | LibPart | Footprint
1 | 2 | C1, C4 | 22uF 50V | Device:C_Polarized_US | Capacitor_THT:CP_Radial_D6.3mm_P2.50mm
2 | 2 | C2, C5 | 10uF | Device:C_Polarized_US | Capacitor_SMD:C_0603_1608Metric_Pad1.08x0.95mm_HandSolder
3 | 2 | C3, C6 | 0.1uF | Device:C_Polarized_US | Capacitor_SMD:C_0603_1608Metric_Pad1.08x0.95mm_HandSolder
4 | 3 | C7, C9, C14 | 0.1uF | Device:C | Capacitor_SMD:C_0603_1608Metric_Pad1.08x0.95mm_HandSolder
5 | 1 | C8 | 2.2uF | Device:C | Capacitor_SMD:C_0603_1608Metric_Pad1.08x0.95mm_HandSolder
6 | 1 | C10 | 10nF | Device:C | Capacitor_SMD:C_0603_1608Metric_Pad1.08x0.95mm_HandSolder
7 | 2 | C11, C12 | 0.47uF | Device:C | Capacitor_SMD:C_0603_1608Metric_Pad1.08x0.95mm_HandSolder
8 | 1 | C13 | 1uF | Device:C | Capacitor_SMD:C_0603_1608Metric_Pad1.08x0.95mm_HandSolder
9 | 1 | Conn1 | AndersonPP | MRDT_Connectors:AndersonPP | MRDT_Connectors:Anderson_2_Horizontal_Side_by_Side
10 | 2 | D1, D2 | GREEN | Device:LED | LED_SMD:LED_0603_1608Metric_Pad1.05x0.95mm_HandSolder
11 | 3 | D3, D4, D5 | BLUE | Device:LED | LED_SMD:LED_0603_1608Metric_Pad1.05x0.95mm_HandSolder
12 | 1 | J1 | 6 Pin Molex Micro-Fit | Connector_Generic:Conn_01x06 | Connector_Molex:Molex_Micro-Fit_3.0_43650-0600_1x06_P3.00mm_Horizontal
13 | 1 | J2 | Raspberry Pi - Header Socket | Connector:Raspberry_Pi_2_3 | MRDT_Shields:RaspberryPi_THT_BOTTOM
14 | 1 | JP1 | Solder Jumper | Jumper:SolderJumper_2_Open | Jumper:SolderJumper-2_P1.3mm_Open_RoundedPad1.0x1.5mm
15 | 4 | R1, R5, R6, R7 | 100 | Device:R_US | Resistor_SMD:R_0603_1608Metric_Pad0.98x0.95mm_HandSolder
16 | 1 | R2 | 43 | Device:R_US | Resistor_SMD:R_0603_1608Metric_Pad0.98x0.95mm_HandSolder
17 | 9 | R3, R4, R8, R9, R10, R11, R12, R13, R14 | 4.7k | Device:R_US | Resistor_SMD:R_0603_1608Metric_Pad0.98x0.95mm_HandSolder
18 | 4 | TP1, TP2, TP4, TP5 | TestPoint | Connector:TestPoint | TestPoint:TestPoint_Pad_D2.0mm
19 | 1 | U1 | OKI-5V | MRDT_Devices:OKI | MRDT_Devices:OKI_Horizontal
20 | 1 | U2 | BHI160B | MRDT_Sensors:BHI160B | BHI160B:BHI160B
21 | 1 | U3 | ICM-20608-G | MRDT_Sensors:ICM-20608-G | ICM-20608-G:ICM-20608-G
22 | 1 | U4 | OKI-3V3 | MRDT_Devices:OKI | MRDT_Devices:OKI_Horizontal