## Slide 1: 2023 MRDT Nav Board V2
By Thomas Francois

## Slide 2: 3D Renderings

## Slide 3: 3D Animation

## Slide 4: PCB Structure
3 Modules:
  Teensy Adapter
  Main Board
  Top Board
Boards Joined By Mouse Bites
  Perforations allow separation
4 – Layers
Entire Assembly: 62mm x 90mm

## Slide 5: System Overview
3 Modules
  Teensy Adapter/Shield
    Accesses Teensy pins GPIO pins & Ethernet pins
  Main Board
    Contains Ethernet Jack & OKI Voltage Regulators, along with PowerPole connectors
  Top Board
    Holds both accelerometers & GPS connection

## Slide 6: Teensy Adapter
Teensy GPIO
  2.54mm Pins on Teensy4.1GPIO,
  2.00mm Pins on Teensy4.1 Ethernet
Board Connectors
  2.54mm Sockets for Teensy GPIO
  2.00mm Sockets Teensy Ethernet
2.54mm Pins for mounting below Main Board

## Slide 7: Main Board
Interfaces Ethernet to Teensy
PowerPole connectors to Voltage Regulators
5V and 3V3 OKI Voltage Regulators
  Mount onto Main Board, Top Board lowered onto these pins
Board Connections:
  2.54mm Sockets to Teensy Adapter
  2.54mm Sockets to Top Board

## Slide 8: Top Board
Holds Accelerometers
  ICM-20608 and BHI160B
GPS Connector
  Molex Micro-Fit
Power comes directly from Voltage Regulators
Data routes back to Teensy

## Slide 9: BOM: Same As Before, 2 new parts, & headers
New Additions:
  1 Teensy 4.1
  1 RJ45 (Teensy Recommends Cetus J1B1211)
  2.54mm Headers
    4x) 1 by 24 Sockets
    4x) 1 by 24 Pins
    2x) 1 by 3 Sockets
    2x) 1 by 16 Sockets
    2x) 1 by 16 Pins
    1x) 2 by 3 Pins
    1x) 2 by 3 Sockets
  2.00mm Headers
    1x) 2 by 3 2.00mm Pins
    1x) 2 by3 2.00mm Sockets

## Slide 10: Still To Do
Ethernet Header between Teensy and Adapter Board are misaligned.
Need to decide upon mounting style.
Alternate Layouts:
  Teensy between Teensy Adapter and Main Board, instead of on bottom
  Items on Top Board moved onto Adapter Board